## Slide 1: Copernicus: "Question your assumptions"
Sam Cornwell, John Butterworth, Xeno Kovah, Corey Kallenberg, Amy Herzog

## Slide 2: Motivations
The BIOS is the first code to execute on your CPU. It's security-critical, and if it's damaged, the system won't boot (DoS)
Because no one is looking at the BIOS, it is a great place to persist indefinitely without fear of detection
Measurement leveraging a trusted platform module (TPM) is a good first step, but we don't know how good measurement implementations are without analyzing them
  An implementation we've looked at was not good.
  We will talk about that at BlackHat Las Vegas 2013
Notes: Because we like you.

## Slide 3: Motivations 2
When TPM measurements say something changed unexpectedly, we'd like to know more specifically what changed in which component, and ideally what the security implications are
We'd also like to know proactively if a given system is vulnerable to malicious BIOS modification, and if there are any updates that correct the configuration and increase the protection
Notes: Because we like you.

## Slide 4: x86 Architecture Overview
SPI Flash
System RAM
BIOS Region Begin
0
4GB
www.intel.com/.../datasheet/io-controller-hub-9-datasheet.pdf
Notes: Talk through this fairly slow, because it's going to be way new for most of the audience.
www.intel.com/.../datasheet/io-controller-hub-9-datasheet.pdf
Modified slightly by moving the TPM to a more visible location (removed the clocks – hey who needs those!)

## Slide 5: Boot Sequence
Boot Block
SPI Flash
System RAM
Configuration
Modules
…
FFFF_FFF0
0
4GB
BIOS Region Begin
Boot Block
High "Memory"

## Slide 6: TPM Measurement
Boot Block
SPI Flash
System RAM
…
hashing
TCG Measure (SRTM)
PCR Extend (hash)
0
4GB
PCR0=SHA1(020 | hash)
Boot Block
High "Memory"

## Slide 7: What If a PCR Changes?
If a difference is found, now what are you going to do?
We want to be able to attribute changes in a hash to specific locations in the BIOS image that changed.
We need to be able to compare the before and after raw BIOS dumps. We can then say something about the purpose of the location where the change occurred, and whether it's expected or not.
  This helps tamp down false positives
Copernicus gives us BIOS dump capability!

## Slide 8: Running Copernicus Video
standalone.bat
http://youtu.be/zZe88jW9PuE
Notes: Compare two of the same machines over time, and show correlation to the UEFI flash filesystem.
Show one example which is "natural" changes between runs/reboots

## Slide 9: Running Copernicus 2

## Slide 10: Running Copernicus 3 – .csv output

## Slide 11: Running Copernicus 4 – .log output

## Slide 12: BIOS Change Detection Video
bios_diff.py
http://youtu.be/XaeMrL1LqPo
Notes: Compare two of the same machines over time, and show correlation to the UEFI flash filesystem.
Show one example which is "natural" changes between runs/reboots

## Slide 13: PCR Change Response with Copernicus
Now when a BIOS change is found it can be in detail, and most importantly it is now actionable.
UEFI firmware is compiled from C code into Microsoft's Portable Executable format.
Therefore Windows reverse engineering skills from other people (such as malware analysts) can be reused to understand UEFI changes.
  "Just" need to read some UEFI specs
We will be making classes to help existing reverse engineers be able to understand UEFI binaries, and posting them to OpenSecurityTraining.info in the future

## Slide 14: BIOS Static Analysis in IDA Video
IDA Pro
http://youtu.be/R-5UO6jLkEI
Notes: Compare two of the same machines over time, and show correlation to the UEFI flash filesystem.
Show one example which is "natural" changes between runs/reboots

## Slide 15: BIOS Static Analysis in IDA 2
Clean BIOS TPM module entry point
Attacked BIOS TPM module entry point
A single byte change means the TPM module will immediately return, and never initialize the TPM for early-system use

## Slide 16: BIOS Static Analysis in IDA 3
UEFI BIOSes make use of a number of specified data structures. Snare extracted some of these structures into "behemoth.h", which can then be imported into IDA

## Slide 17: BIOS Static Analysis in IDA 4
Because the BIOS is written in 32 bit C, Hexrays can be used to decompile
When we apply structure definitions from behemoth.h, we now know the function which is being called; in this case, InstallPpi()

## Slide 18: BIOS Static Analysis in IDA 5
This translates to
If(LocatePpi() succeeds){
GetBootMode()
do some other functions
InstallPpi()
etc
}
Which is much easier to read than a bunch of handcoded assembly
Some other pseudocode made more readable thanks to applying structures

## Slide 19: BIOS Static Analysis in IDA 6
If we have data locations which the structures say are UEFI_GUIDs
We can look the GUID up in a list of GUIDs extracted from the UEFI reference implementation and see if it's a well-known GUID
In this case, if we didn't already suspect this module had to do with the TPM, the fact that it's installing a PPI named "TPM_INITIALIZED" would be a dead giveaway.

## Slide 20: BIOS Access Control Checking
Besides being able to detect potential BIOS implants, we would like to know how vulnerable a BIOS is to being written
BIOS makers are supposed to set certain access control bits that are scattered around a number of hardware registers. These bits should make it so that no one can write to the BIOS flash chip until next reboot.
Unfortunately vendors don't always set these bits correctly, and the BIOS can therefore be written to directly by anyone with admin privileges
Copernicus checks these bits and reports whether a BIOS flash chip is open for modification
Notes: http://cdn3.iconfinder.com/data/icons/humano2/128x128/stock/stock_lock-open.png

## Slide 21: BIOS/SMRAM Writability Analysis Video
protections.py
http://youtu.be/KhwKN0868FI
Notes: Compare two of the same machines over time, and show correlation to the UEFI flash filesystem.
Show one example which is "natural" changes between runs/reboots

## Slide 22: Example Analysis Results
We've tested on ~3700 machines from various organizations so far
~38% have unlocked BIOS
COUNT | BIOS_VENDOR | PRODUCT_NAME | BIOS_VERSION | SMRAM_UNLOCKED | BIOS_UNLOCKED
7 | Dell Inc. | Latitude E6400 | A25 | 0 | 7
3 | Dell Inc. | Latitude E6400 | A27 | 0 | 3
10 | Dell Inc. | Latitude E6400 | A29 | 0 | 10
7 | Dell Inc. | Latitude E6400 | A30 | 0 | 0
1 | Dell Inc. | Latitude E6400 | A31 | 0 | 0
2 | Dell Inc. | Latitude E6400 | A32 | 0 | 0
1 | Dell Inc. | Latitude E6400 | A33 | 0 | 0
Notes: Note that this also shows how when you upgrade to a high enough BIOS revision, the BIOS stops being vulnerable.

## Slide 23: Possible Defenses
For some machines (such as the Dell E6400), newer BIOS updates have the access controls set
  Rev A29 is open & vulnerable, Rev A30 and newer aren't
We are collecting a more comprehensive matrix of which models and BIOS revisions are secure
This can be the basis for determining whether to perform enterprise-wide BIOS updates
When we find enough machines for which there is no BIOS update fix, we can go to the vendor and ask them to fix this
Notes: http://www.iconfinder.com/icondetails/115716/128/lock_password_secure_security_unlock_icon

## Slide 24: Tech Transfer
Also looking for government entities interested in knowing whether their BIOSes are currently open and vulnerable
  We already have an installer that runs through HBSS for easy deployment in DoD environments
We are looking for vendors to incorporate the capabilities into their agent-based security software
  The licensing will be "we give you code, you tell us how many machines you've seen that have writable BIOS"
  Already talking with McAfee, Wave, and Crowdstrike
    You don't want to fall behind them do you? :)
Contact Xeno if interested in piloting/licensing Copernicus

## Slide 25: Conclusion
The raw BIOS dumping capability gives more detailed and actionable information about BIOS changes
Configuration data helps to determine writable (vulnerable) BIOS configurations
We're enabling the collection of this data, but we need to find more hosts to deploy to
No one knows how common writable BIOSes are in the wild
We think it's going to turn out that BIOSes are much more vulnerable than people have assumed

## Slide 26: Questions?
scornwell@mitre.org
xkovah@mitre.org
P.s. to learn more about TPMs, reverse engineering, and in the future, BIOS, check out the free and open source classes at OpenSecurityTraining.info
If you already know the classes, take the material and teach!