## Slide 2: Do You Like Coffee With Your Dessert? Java and The Raspberry Pi
Simon Ritter
Java Technology Evangelist
Twitter: @speakjava

## Slide 3
The following is intended to outline our general product direction. It is intended for information purposes only, and may not be incorporated into any contract. It is not a commitment to deliver any material, code, or functionality, and should not be relied upon in making purchasing decisions. The development, release, and timing of any features or functionality described for Oracle’s products remains at the sole discretion of Oracle.

## Slide 4: Program Agenda
The Raspberry Pi
ARM Processors
Java on ARM and the Raspberry Pi
Using Java on the Raspberry Pi
Demos

## Slide 5: The Raspberry Pi

## Slide 6: Raspberry Pi
Project started in 2006
  Goal was to devise a computer to inspire children
  Inspiration from the BBC Micro project from 1981
History and Goals

## Slide 7: Raspberry Pi
Officially launched on Febuary 29th 2012
  First production run was 10,000 boards
  Both RS and Farnell’s servers were stalled on the day of launch
  RS reported over 100,000 pre-orders in one day
  Current production is about 4,000 boards per day
    Originally in China, now by Sony in the UK
  Current estimate is that around 1 million boards sold so far
History and Goals

## Slide 8: Raspberry Pi
CPU: ARM 11 core running at 700MHz
  Broadcom SoC package
  Can now be overclocked to 1GHz (without breaking the warranty!)
Memory: 256Mb 512Mb
I/O:
  HDMI and composite video
  Audio out (3.5mm plug)
  2 x USB ports (Model B only)
  Ethernet (Model B only)
  Header pins for GPIO, UART, SPI and I2C
Specification

## Slide 9: ARM Architecture

## Slide 10: A Brief (But Interesting) History Lesson
Acorn BBC Micro (6502 based)
  Not powerful enough for Acorn’s plans for a business computer
Berkeley RISC Project
  UNIX kernel only used 30% of instruction set of Motorola 68000
  More registers, less instructions (Register windows)
  One chip architecture to come from this was… SPARC
Acorn RISC Machine (ARM)
  32-bit data, 26-bit address space, 27 registers
  First machine was Acorn Archimedes
Spin off from Acorn, Advanced RISC Machines

## Slide 11: ARM Features
32-bit RISC Architecture
  ARM accounts for 75% of embedded 32-bit CPUs today
  8 billion chips sold last year, more than 30 billion in total
    zero manufactured by ARM
Abstract architecture and microprocessor core designs
  Raspberry Pi uses an ARM11 with the ARMv6 instruction set
Low power consumption
  Good for mobile devices
  Raspberry Pi can be powered from 700mA 5V only PSU
  Raspberry Pi does not require heatsink or fan

## Slide 12: Current ARM Technology
ARMv6
  ARM 11, ARM Cortex-M
ARMv7
  ARM Cortex-A, ARM Cortex-M, ARM Cortex-R
ARMv8 (Announced)
  Will support 64-bit data and addressing
  32-bit instructions, 30 registers

## Slide 13: Java On The ARM and Raspberry Pi

## Slide 14: Java Specifics For ARM
Despite being an ARMv6 processor it does include an FPU
  FPU only became standard as of ARMv7
FPU (Hard Float, or HF) is much faster than a software library
Linux distros and Oracle JVM for ARM assume no HF on ARMv6
  Need special build of both
  Raspbian distro build now available
  Oracle JVM just released (Early Access)
Floating Point Operations

## Slide 15: Beyond RISC
DSP Enhancements
Jazelle
Thumb / Thumb2 / ThumbEE (Reduced instruction set RISC)
  Better code density
Floating Point (VFP)
NEON
Security Enhancements (TrustZone)
  2 Virtual processors (mode switch)
  Hardware based access control
Performance Improvements
Notes: Thumb – making code more condensed. Thumb =16bit, thumb 2 = 32 bit, thumb extended execution good for JIT type compilation
NEON enhanced SIMD (Single Instruction, multiple data) Media Processing Engine, optimised for media
TrustZone adds an extra bit to indicate security.

## Slide 16: JDK8 Early Access
Released at end of 2012
Hard floating point support compiled in
Includes JavaFX libraries
Tested specifically for the Raspberry Pi
Java SE 7 to follow at a later date
Official Java For The Raspberry Pi

## Slide 17: Java ME Embedded 3.3
Intended for small footprint devices
  10s of Mb RAM
  Low power processor
Raspberry Pi is cheap platform to start development
Includes Device Access API
  GPIO, SPI, I2C, UART support
Raspberry Pi Version

## Slide 18: Using Java on the Raspberry Pi

## Slide 19: Making A Noise With Java
Sound drivers now included in distros
Java Sound API
  Remember to add audio to user’s groups
  modprobe snd_pcm_oss
    creates /dev/dsp, needed by MIDI interface
  Some bits work, others not so much
    Playing (the right format) WAV file works
    MIDI seems unbelievably slow
FreeTTS text-to-speech
  Some bits working (limited domain voice)

## Slide 20: JavaFX on the Raspberry Pi
Work involves optimal implementation of Prism graphics engine
  Take advantage of Videocore 4 GPU
Configure with -Djavafx.platform
  x11 (X11, software rendering) No X11 support
  eglfb (OpenGL rendering to framebuffer) (JDK8 EA)
Some things not supported
  Media
  WebEngine, WebView
  Some IO still needs work (gamepad)

## Slide 21: Using The Serial Port
UART provides TTL level signals (3.3V)
RS-232 uses 12V signals
Use MAX3232 chip to convert
Use this for access to serial console
Serial port connectivity
  /dev/ttyAMA0

## Slide 22: The Talking Raspberry Pi
SP03 text to speech board
  Connected to UART via RS-232
Disable console output
  Edit /etc/inittab
    Comment out getty /dev/ttyAMA0
  Edit /boot/cmdline.txt
    remove console and kgdboc references
38,400 baud, 8 Bit, 2 stop bits, no parity
Simple byte sequence to send text to the board
+5V
GND
TX
RX

## Slide 23: USB Peripherals
Easy devices are ones that appear as simple serial devices
  /dev/ttyUSB0
More complex devices need native code and libusb
  apt-get install libusb-1.0-0-dev
Universal Serial Bus (But not as simple as serial)

## Slide 24: Java and Serial Port/USB Serial Device
Install RXTX package
  apt-get install librxtx-java
How to solve the /dev/ttyS* only problem
  System.setProperty(“gnu.io.rxtx.SerialPorts”,
  “/dev/ttyUSB0”);
  System.setProperty(“gnu.io.rxtx.SerialPorts”,
  “/dev/ttyAMA0”);
JavaComm API

## Slide 25: The OWI Robot Arm
Comes with USB interface
  Windows only driver
  Recognized as USB device by Linux
Use native code for control and JNI
Simple control protocol
  3 bytes (1 = arm, 2 = base, 3 = light)
  Combining movements requires some bit twiddling
  Can only stop all motors, not individually
Cheap and cheerful

## Slide 26: Robot Arm Control
Native C functions
  Initialisation of arm using libusb and appropriate device
  Separate function for each control element
  Compile to shared library
Use JNI to generate header file appropriate to Java code usage
  e.g. native int arm_usb_init()
  Implement appropriate stub to call library
  Compile to shared library
  JNI can be fiddly
JNI Code

## Slide 27: Robot Arm Control
Java code is simple
  Calibration required to determine time for specific movement
Java Code
arm_gripper_move(OPEN);
uSleep(500);
arm_gripper_move(STOP);
uSleep(500);
arm_gripper_move(CLOSE);
uSleep(500);
arm_gripper_move(STOP);

## Slide 28: Gamepad Controller
Manual dexterity
Linux supports most of these out of the box
Drivers create entries in /dev/input
Java API through Jinput
  Mature technology (not been touched since 2003)
  Recompile code on RasPi
  Needed to tweak build script for incomplete classpath
    EVIOCGUSAGE disappeared
    Rename libjinput-linux.so to libjinput-linux64.so
  Devices do not have general read/write access
    Possible (but frustratingly difficult) to use udev.rules to fix this

## Slide 29: Gamepad Controller
Wrote library on top of JInput
  JInput too generic, needed code to be more specific to gamepad
Code
GamePadController gpc = new GamePadController();
gpc.addButtonListener(GamePadController.BUTTON_1, this);
gpc.addJoystickListener(GamePadController.JOYSTICK_LEFT, this);
new Thread(gpc).start();

## Slide 30: Gamepad Controller
Code
public void buttonAction(ButtonEvent be) {
if (be.getId() == GamePadController.BUTTON_1)
robotArm.setGripperLight(true);
...
}
public void joystickAction(JoystickEvent jse) {
if (jse.getId() == GamePadController.JOYSTICK_LEFT) {
if ((position & JoystickEvent.POSITION_LEFT) != 0)
robotArm.moveElbow(ArmController.UP);
}
...
}

## Slide 31: Mind Controlled Raspberry Pi
Neurosky headset
Bluetooth USB dongle
  Serial communications
Custom Java library to gather data

## Slide 32: Using The GPIO Lines
P1 Connector Layout (REV 1)
P1-01
5V
GND
0 (SDA)
1 (SCL)
14 (TXD)
15 (RXD)
18
23
24
25
8
7
10 (MOSI)
9 (MISO)
11 (SCLK)
22
21
17
4
3.3V
P2 Connector: Pin 1 = 3.3V Pin 7,8 = GND
DNC
DNC
DNC
DNC
DNC
DNC

## Slide 33: Using the GPIO Lines
P1 Connector Layout (Rev 2)
P1-01
5V
GND
0 (SDA)
1 (SCL)
14 (TXD)
15 (RXD)
18
23
24
25
8
7
10 (MOSI)
9 (MISO)
11 (SCLK)
22
27
17
4
3.3V
5V
GND
GND
GND
GND
GND

## Slide 34: Using the GPIO Lines
Magic Incantations
#define BCM2708_PERI_BASE 0x20000000
#define GPIO_BASE (BCM2708_PERI_BASE + 0x200000)
#define BLOCK_SIZE (1024 * 4)
#define PAGE_SIZE (1024 * 4)
/* MMAP */
mem_fd = open(“/dev/mem”, O_RDWR | O_SYNC);
gpio_mem = malloc(BLOCK_SIZE + (PAGE_SIZE – 1));
gpio_map = (unsigned char *)mmap(
(caddr_t)gpio_mem, BLOCK_SIZE, PROT_READ | PROT_WRITE,
MAP_SHARED | MAP_FIXED, mem_fd, GPIO_BASE);
gpio = (volatile unsigned *)gpio_map;

## Slide 35: Using the GPIO Lines
More Magic Incantations
/* Pin input */
*(gpio + (pin / 10)) &= ~(7 << ((pin % 10) * 3));
/* Pin output */
*(gpio + (pin / 10)) &= ~(7 << ((pin % 10) * 3));
*(gpio + (pin / 10)) |= (1 << ((pin % 10) * 3));
/* Pin high */
*(gpio + 7) = 1 << pin;
/* Pin low */
*(gpio + 10) = 1 << pin;

## Slide 36: Hide The Magic Incantations With JNI
Access to /dev/mem needs root access
  Could solve this by writing our own device driver
Simple Java Interface
gpio_init();
gpio_pin_output(MOTOR_PIN_CLKWISE);
gpio_pin_output(MOTOR_PIN_ACLKWISE);
/* Turn clockwise */
gpio_pin_low(MOTOR_PIN_ACLKWISE);
gpio_pin_high(MOTOR_PIN_CLKWISE);

## Slide 37: Pi4J
Bridge between native code and Java
  GPIO
  I2C
  SPI
GPIO code is simple and easy to use
Still needs root access
Still in development
  Current version 0.0.4
Simpler IO

## Slide 38: GPIO Example: LEGO Motors
Using L293D Dual H-Bridge
GPIO line
GPIO line
GPIO line
GPIO line
+9V Supply

## Slide 39: How to Use SPI and I2C
Drivers still experimental
  Check Chris Boot’s blog (www.bootc.net)
Devices for SPI
  /dev/spidev-0.0 and /dev/spidev-0.1
Devices for I2C
  Run i2c-dev
  /dev/i2c-0
Not yet tried these with Java (Screen and JavaFX project next)
Even more complex peripherals

## Slide 40: Current Project
In Car Raspberry Pi with JavaFX

## Slide 41: Conclusions
Raspberry Pi is a very cool (and cheap) computer
  Great for teaching
  Great introduction to ARM
Java works well and will get better
Opportunities are limitless!

## Slide 42: Further Information
java.oracle.com
www.oracle.com/technetwork/java/embedded
Raspberry Pi User Guide – Eben Upton, Gareth Halfacree
www.raspberrypi.org
blogs.oracle.com/speakjava

## Slide 43
Demos