## Slide 2: Porting JavaFX Embedded
Lisa Selle
Principal Member of Technical Staff
JavaFX Embedded
September 29, 2014
Copyright © 2014, Oracle and/or its affiliates. All rights reserved.
Notes: This is a Title Slide with Java FY15 Theme slide ideal for including the Java Theme with a brief title, subtitle and presenter information.
To customize this slide with your own picture:
Right-click the slide area and choose Format Background from the pop-up menu. From the Fill menu, click Picture and texture fill. Under Insert from: click File. Locate your new picture and click Insert.
To copy the Customized Background from Another Presentation on PC
Click New Slide from the Home tab's Slides group and select Reuse Slides.
Click Browse in the Reuse Slides panel and select Browse Files. Double-click the PowerPoint presentation that contains the background you wish to copy.
Check Keep Source Formatting and click the slide that contains the background you want.
Click the left-hand slide preview to which you wish to apply the new master layout.
Apply New Layout (Important): Right-click any selected slide, point to Layout, and click the slide containing the desired layout from the layout gallery.
Delete any unwanted slides or duplicates.
To copy the Customized Background from Another Presentation on Mac
Click New Slide from the Home tab's Slides group and select Insert Slides from Other Presentation…
Navigate to the PowerPoint presentation file that contains the background you wish to copy. Double-click or press Insert. This prompts the Slide Finder dialogue box.
Make sure Keep design of original slides is unchecked and click the slide(s) that contains the background you want. Hold Shift key to select multiple slides.
Click the left-hand slide preview to which you wish to apply the new master layout.
Apply New Layout (Important): Click Layout from the Home tab's Slides group, and click the slide containing the desired layout from the layout gallery.
Delete any unwanted slides or duplicates.

## Slide 3
Notes: This is a Safe Harbor Front slide, one of two Safe Harbor Statement slides included in this template.
One of the Safe Harbor slides must be used if your presentation covers material affected by Oracle’s Revenue Recognition Policy
To learn more about this policy, e-mail: Revrec-americasiebc_us@oracle.com
For internal communication, Safe Harbor Statements are not required. However, there is an applicable disclaimer (Exhibit E) that should be used, found in the Oracle Revenue Recognition Policy for Future Product Communications. Copy and paste this link into a web browser, to find out more information.
http://my.oracle.com/site/fin/gfo/GlobalProcesses/cnt452504.pdf
For all external communications such as press release, roadmaps, PowerPoint presentations, Safe Harbor Statements are required. You can refer to the link mentioned above to find out additional information/disclaimers required depending on your audience.

## Slide 4: Program Agenda
JavaFX Embedded 8u6 reference implementation
JavaFX embedded porting overview
Porting JavaFX embedded to a new platform
Monocle – the new JavaFX embedded porting layer
Creating a new Monocle implementation
1
2
3
5
4

## Slide 5: Program Agenda
JavaFX Embedded 8u6 reference implementation
JavaFX embedded porting overview
Porting JavaFX embedded to a new platform
Monocle – the new JavaFX embedded porting layer
Creating a new Monocle implementation
1
2
3
4
5

## Slide 6: JavaFX Embedded 8u6 Reference Implementation
Full screen framebuffer
  Provides for multiple stages/windows without an OS-level window manager
Supports both hardware-accelerated rendering and software fallback
Supports Linux input
  Keyboards
  Mouse
  Touch and multi-touch devices
What is provided

## Slide 7: JavaFX Embedded 8u6 Reference Implementation
Supported platforms:
  Freescale i.MX6 Sabre Device Platform (Hard-float ABI)
Known to work:
  Raspberry Pi model B (Hard-float ABI)
  Beagleboard XM rev C (Soft-float)
Current Platforms

## Slide 8: JavaFX Embedded 8u6 Reference Implementation
Reference build using Linux desktop tools
  Gradle 1.4
  GCC 4.7.2
  Platform SDK for headers/system libraries (for cross build)
OpenJFX wiki has documentation for arm hard float cross build
  https://wiki.openjdk.java.net/display/OpenJFX/Main
Building JavaFX Embedded (OpenJFX)

## Slide 9: Program Agenda
JavaFX Embedded 8u6 reference implementation
JavaFX embedded porting overview
Porting JavaFX embedded to a new platform
Monocle – the new JavaFX embedded porting layer
Creating a new Monocle implementation
1
2
3
4
5

## Slide 10: JavaFX Embedded Porting Overview
Why is porting required?
  EGL framebuffer initialization is not standardized across platforms
  Framebuffer layer management is not standardized across platforms
  Allows support for new input devices to be added

## Slide 11: JavaFX Embedded Porting Overview
RAM
  JavaVM + JavaFX requires 34MB ram minimum
  More memory will be needed depending on the size and complexity of the application
ROM
  JavaVM Compact1 profile with JavaFX Graphics requires 18MB minimum
  More storage will be needed depending on the size and complexity of the application
Target platform requirements

## Slide 12: JavaFX Embedded Porting Overview
VRAM
  VRAM requirements can be high, particularly if large images are used
  VRAM is also consumed by fonts and gradients
  JavaFX has mechanisms to allow it try to work within VRAM limits; this can be specified on the command line
  More information on OpenJFX wiki
Target platform requirements

## Slide 13: JavaFX Embedded Porting Overview
Operating system for the target device (reference implementation assumes Linux; other operating systems could be supported)
Native drivers for any input devices you wish to support
Font support
  Freetype/pango libraries
  A port could add an alternative font engine which may have other native requirements
Java runtime environment (JRE) version 8 or better
Target platform requirements (continued)

## Slide 14: JavaFX Embedded Porting Overview
Framebuffer management, either:
  Direct framebuffer, full screen access
    EGL drivers that support direct access to the framebuffer
    OpenGL ES drivers for hardware accelerated graphics
    Software fallback is available if hardware acceleration is not available
  System-provided window management
    GTX for X11
    EGL/GLX OpenGL/OpenGL ES drivers
Target platform requirements (continued)

## Slide 15: Program Agenda
JavaFX embedded 8u6 reference implementation
JavaFX embedded porting overview
Porting JavaFX embedded to a new platform
Monocle – the new JavaFX embedded porting layer
Creating a new Monocle implementation
1
2
4
5
3

## Slide 16: Porting JavaFX Embedded to a New Platform
Operating system setup can be a very challenging part of a new port
  It can be difficult to find an integrated OS with all the necessary pieces; it’s often necessary to build it up piecemeal, beginning with an OS then adding vendor-specific drivers and libraries
  Documentation on platform-specific features such as EGL initialization and framebuffer layer management (where available) can be difficult to come by
Non-linux operating systems will present additional challenges; plan for additional efforts on fonts, cursors, input, and build setup
Operating System

## Slide 17: Porting JavaFX Embedded to a New Platform
Obtain cross compiler and development tools
Read the build section on OpenJFX wiki
Using this as a guide, you will need to create a new build profile for your platform
  Provides paths to compiler and build tools, specifies build/link flags
  Toggles the build options
Build Setup

## Slide 18: Porting JavaFX Embedded to a New Platform
Current choices for window management:
  Glass/GTK with X11
  Monocle
    Provides management for multiple stages/window
    Does not provide any mechanism for interaction with other native windows (assumes full-screen ownership)
    Provides mechanism for platform-specific initialization of drawing surfaces, input device management, and cursor handling
  Custom
    Roll your own! If you need to interact with a native window manager other than X11
Window Management

## Slide 19: Program Agenda
JavaFX embedded 8u6 reference implementation
JavaFX embedded porting overview
Porting JavaFX embedded to a new platform
Monocle – the new JavaFX embedded porting layer
Creating a new Monocle implementation
1
2
4
5
3

## Slide 20: Monocle – the New JavaFX Embedded Porting Layer
Glass implementation for systems that do not have an underlying window manager
Written almost entirely in java (previous porting layer, lens, relied heavily on native code)
What is Monocle?

## Slide 21: Monocle – the New JavaFX Embedded Porting Layer
Functional and quality parity with lens on all platforms
Simplify the process of porting to a new platform
Minimize native code
Improve maintainability and debuggability of embedded ports
Pluggability of Linux input device handlers
What are the goals of Monocle?

## Slide 22: Monocle – the New JavaFX Embedded Porting Layer
Glass integration classes (MonocleApplication, MonocleWindow, MonocleView) - interface with the rest of glass. These classes run on the application thread.
Window management classes (MonocleWindow, MonocleWindowManager) – manage window state of individual windows and z-order of the window stack. These classes run on the application thread.
Generic components of Monocle

## Slide 23: Monocle – the New JavaFX Embedded Porting Layer
Input device management (InputDeviceXXX, InputDeviceRegistry) – InputDevices represent individual devices and deliver their associated events. The input device registry manages all input devices. The generic input device code runs on the application thread.
Input handling (MouseInput/State, TouchInput/State, KeyInput/State) – process various types of input. These classes run on the application thread.
Platform – abstract out the platform-specific functionality, such as initialization of the platform and screen, and management of the cursor (NativePlatform, NativeScreen, NativeCursor).
Generic components of Monocle (continued)

## Slide 24: Monocle – the New JavaFX Embedded Porting Layer
The following monocle platforms are available in the 8u6 release of JavaFX embedded (and also in OpenJFX):
  Linux – generic Linux port, low-level input device nodes and a hardware cursor
  OMAP – for the Beagleboard xM, EGL/framebuffer with Linux device input and a hardware cursor
  MX6 – for the Freescale i.MX6, EGL/framebuffer with Linux device input and a hardware cursor
  OMAPX11 – for the Beagleboard xM, EGL/X11 with Linux device input and a hardware cursor
Available monocle platforms

## Slide 25: Monocle – the New JavaFX Embedded Porting Layer
The following monocle platforms are available in the 8u6 release of JavaFX embedded (and in OpenJFX):
  DISPMAN – for the Raspberry Pi, with Linux device input and a hardware cursor
  X11 – for generic Linux/X11 platforms, using X11 for input and cursor
  Headless – provides neither input nor output. Used mainly for testing.
Other platforms which should fit but are not yet available:
  Android
Available monocle platforms (continued)

## Slide 26: Monocle – the New JavaFX Embedded Porting Layer
While most of Monocle is written in Java, there are some classes which use JNI to access native C APIs:
  C.java – provides access to C data structures. Requires loadLibrary* permission
  LinuxSystem.java – provides access to selected Linux APIs. Requires loadLibrary* permission
  X.java – provides access to X11 APIs
  EGL.java – provides access to EGL APIs
Native Code in Monocle

## Slide 27: Program Agenda
JavaFX embedded 8u6 reference implementation
JavaFX embedded porting overview
Porting JavaFX embedded to a new platform
Monocle – the new JavaFX embedded porting layer
Creating a new Monocle implementation
1
2
4
5
3

## Slide 28: Monocle – the New JavaFX Embedded Porting Layer
To create a new Monocle implementation, you will need to provide platform-specific subclasses of:
  NativeScreen
  AcceleratedScreen (if you wish to support hardware-accelerated rendering)
  NativeCursor (if you are using a pointing device and wish to support hardware-accelerated rendering)
  InputDeviceRegistry
  NativePlatform
  NativePlatformFactory
Creating a new Monocle implementation

## Slide 29: Monocle – the New JavaFX Embedded Porting Layer
Provides information about the screen it is using, and blits pixels to the screen in the software rendering path
Often this class is based on a Linux framebuffer but could be based on something else
  Example: X11Screen – creates a single X window and renders into it
Creating a new Monocle implementation - NativeScreen

## Slide 30: Monocle – the New JavaFX Embedded Porting Layer
Provides a way to get an OpenGL ES context to the screen
Typically uses EGL API to create a drawing surface
EGL requires a NativeWindowType parameter whose meaning varies from platform to platform
The method used to obtain this parameter typically needs to be customized for each new port
Creating a new Monocle implementation - AcceleratedScreen

## Slide 31: Monocle – the New JavaFX Embedded Porting Layer
Not needed for software rendering platforms (a SoftwareCursor is supplied)
Method for getting a hardware cursor to the screen is very platform dependent; for example:
  On TI OMAP3 devices, /dev/fb1 framebuffer overlay can be configured and used for the cursor
  On Raspberry PI the dispman API can be used to create a separate graphics layer for the cursor
  On Freescale .iMX6 a framebuffer overlay is used, but the API to access it is different than on the TI OMAP3 devices
Creating a new Monocle implementation - NativeCursor

## Slide 32: Monocle – the New JavaFX Embedded Porting Layer
Handles discovery of input devices
Handles insertion of events from these devices into the JavaFX event queue
Default implementation uses the udev Linux system; other implementations are possible
Creating a new Monocle implementation - InputDeviceRegistry

## Slide 33: Monocle – the New JavaFX Embedded Porting Layer
NativePlatformFactory – creates the NativePlatform implementation. The NativePlatformFactory whose match algorithm returns true for a particular platform is the one which will be selected.
The match algorithm can be based on various things – existence of specific system files, particular symbols present in a native library, etc.
NativePlatform – bundles together the NativeScreen, NativeCursor, and InputDeviceRegistry.
NativePlatform and the classes it contains are all singletons.
Creating a new Monocle implementation – NativePlatform, NativePlatformFactory

## Slide 34: Questions?