## Slide 2: Driving the Java Carputer Farther and Faster
(Or Carhacking With Duke)
Simon Ritter
Head of Java Evangelism, Oracle
Twitter: @speakjava
Copyright © 2014, Oracle and/or its affiliates. All rights reserved.
Notes: This is a Title Slide with Java FY15 Theme slide ideal for including the Java Theme with a brief title, subtitle and presenter information.
To customize this slide with your own picture:
Right-click the slide area and choose Format Background from the pop-up menu. From the Fill menu, click Picture and texture fill. Under Insert from: click File. Locate your new picture and click Insert.
To copy the Customized Background from Another Presentation on PC
Click New Slide from the Home tab's Slides group and select Reuse Slides.
Click Browse in the Reuse Slides panel and select Browse Files. Double-click the PowerPoint presentation that contains the background you wish to copy.
Check Keep Source Formatting and click the slide that contains the background you want.
Click the left-hand slide preview to which you wish to apply the new master layout.
Apply New Layout (Important): Right-click any selected slide, point to Layout, and click the slide containing the desired layout from the layout gallery.
Delete any unwanted slides or duplicates.
To copy the Customized Background from Another Presentation on Mac
Click New Slide from the Home tab's Slides group and select Insert Slides from Other Presentation…
Navigate to the PowerPoint presentation file that contains the background you wish to copy. Double-click or press Insert. This prompts the Slide Finder dialogue box.
Make sure Keep design of original slides is unchecked and click the slide(s) that contains the background you want. Hold Shift key to select multiple slides.
Click the left-hand slide preview to which you wish to apply the new master layout.
Apply New Layout (Important): Click Layout from the Home tab's Slides group, and click the slide containing the desired layout from the layout gallery.
Delete any unwanted slides or duplicates.

## Slide 3
Notes: This is a Safe Harbor Front slide, one of two Safe Harbor Statement slides included in this template.
One of the Safe Harbor slides must be used if your presentation covers material affected by Oracle’s Revenue Recognition Policy
To learn more about this policy, e-mail: Revrec-americasiebc_us@oracle.com
For internal communication, Safe Harbor Statements are not required. However, there is an applicable disclaimer (Exhibit E) that should be used, found in the Oracle Revenue Recognition Policy for Future Product Communications. Copy and paste this link into a web browser, to find out more information.
http://my.oracle.com/site/fin/gfo/GlobalProcesses/cnt452504.pdf
For all external communications such as press release, roadmaps, PowerPoint presentations, Safe Harbor Statements are required. You can refer to the link mentioned above to find out additional information/disclaimers required depending on your audience.

## Slide 4: Program Agenda
Introduction to the Carputer
More data
Heads up display/telematics
Driver analysis
Conclusions and resources
Demos
1
2
3
4
5
6

## Slide 5: Introduction to the Carputer
Notes: This slide can also be used as a Q and A slide

## Slide 6: How Cars Used To Be
Zero lines of code

## Slide 7: Last Years Carputer

## Slide 8: Last Year’s UI

## Slide 9: Ideas For A Better Carputer
More car data via the CAN bus
  Steering angle, gear selected, ABS data (individual wheel speed)
  Controls (steering wheel buttons, indicators)
GPS data
Heart rate monitor for driver
Tyre pressure monitoring
Thermal sensor for brake or tyre temperature

## Slide 10: Ideas For A Better Carputer
Different display method
  Heads up projected onto windscreen
In-car camera recording forward view
Telematics
  GPRS to get driving relevant data (speed limit) from the cloud
Use recorded data to let people post-drive analyse their driving
  Insurance, training applications

## Slide 11: Carputer Architecture Concept
USB via FTDI
Crossover ethernet
Infra red Thermal sensor
CAN High
CAN Low
OBD2 Service Port
Wi-Fi
Accelerometer/Gyro/Compass
I2C
USB
UART
Serial
GPS
Heart Rate Monitor
USB
Video Camera
Raspberry Pi Model B+
7” Touch secreen
USB
SDR/TPMS
CAN Bus

## Slide 12: More Data
Notes: This slide can also be used as a Q and A slide

## Slide 13: Tracking Position With GPS
AdaFruit Ultimate GPS breakout
  10Hz read rate
  Serial interface
Very simple configuration
  Disable /dev/ttyAMA0 on Pi as console
  9600 8N1
  Read data using librxtx-java
  Comma separated values $GPGGA and $GPVTG
  Need to handle frequent data corruption

## Slide 14: Heart Rate Monitoring of the Driver
Sparkfun board
  USB interface, serial connection
Similar to GPS
  Use librxtx-java
  9600, 8N1
More complicated coding
  Actually need to send a read request!
Some issues with wireless connection
  80cm max, doesn’t work well through a Rapsberry Pi

## Slide 15: In-car Video
Becoming very common to avoid insurance issues
Transcend DrivePro 200
  Built-in Wi-Fi
  iPhone app
How to get video stream?
  Approached Transcend tech support
  Found VLC code
  Wireshark
  SYN/ACK, Yuck!
Camera | Application
192.168.0.1 | 192.168.0.2
Port 9000 | Port 43229
Port 9001 | Port 42719
Port 9002 | Port 58105
Port 8554 (RTSP) | Port 60583

## Slide 16: The Simplest Solution Is Often The Best
Push button using GPIO lines and Pi4J

## Slide 17: Tyre Pressure Monitoring System (TPMS)
All US vehicles must have a TPMS
  Post-Firestone issues
  TREAD act
Not mandatory in EU
  My Audi has TPMS based on ABS sensors
    Tyre deflates, wheel gets smaller, detect speed differential
After market TPMS are cheap
Notes: TREAD Transportation Recall Enhancement Accountability and Documentation Act

## Slide 18: TPMS Decoding
Bought some sensors on eBay
  Documentation states they use 433MHz
  Dismantle them to find they use an SP37 chip from Infineon
Software Defined Radio (SDR) receiver
  eBay, $20
rtl_433 software from Github
  Now for the fun part
Unfortunately, unable to decode data
  Need to look at GNU Radio (future project)

## Slide 19: Thermal Sensors For Brakes and Tyres
The Goal

## Slide 20: Infra-Red Thermometer
MLX90614 breakout board
  I2C interface seemed problematic on the Pi
  Also has serial interface
  Use FTDI breakout board
  4 wires becomes simple serial interface
The Reality

## Slide 21: Thermal Sensor Data
Provides continuous reading as lines of text (e.g. 73.2F)
  Don’t like Fahrenheit, wanted Celcius
  Lambdas and Streams!
private double currentTemperature;
public void run() {
thermalReader.lines()
.mapToDouble(s -> Double.parseDouble(s.substring(0, s.length() - 1)))
.map(t -> ((t - 32) * 5 / 9))
.filter(t -> t != currentTemperature)
.peek(t -> listener.ifPresent(l -> l.temperatureChange(t)))
.forEach(t -> currentTemperature = t);
}

## Slide 22: Thermal Sensor Data
Provides continuous reading as lines of text (e.g. 73.2F)
  Don’t like Fahrenheit, wanted Celcius
  Lambdas and Streams!
private double currentTemperature;
public void run() {
thermalReader.lines()
.mapToDouble(s -> Double.parseDouble(s.substring(0, s.length() - 1)))
.map(t -> ((t - 32) * 5 / 9))
.filter(t -> t != this.currentTemperature)
.peek(t -> listener.ifPresent(l -> l.temperatureChange(t)))
.forEach(t -> this.currentTemperature = t);
}

## Slide 23: Fitting The Thermal Sensors
Tyre Sensor

## Slide 24: Fitting The Thermal Sensors
Brake Disk Sensor

## Slide 25: Fitting The Thermal Sensors
Separate Pi in Engine Bay

## Slide 26: Fitting The Thermal Sensors
Simple server listens on port
Carputer requests data
Couple of issues
  Server needed reset for new connection (bug to be fixed)
  How to tell which sensor is which (ttyUSB0/ttyUSB1)
The Networked Car

## Slide 27: Fitting The Thermal Sensors
Rasperry Pi at over 50C
  After 10 minute drive
New approach required
  Longer USB cables
  Put the Pi in the car
Internal Combustion Produces Heat

## Slide 28: Getting Data From The CAN Bus
Controller Area Network
Used to connect many sensors, actuators and devices
  Without huge amounts of wiring
Conveniently the CAN bus is connected to the OBD2 port
  Yes, the wiring is there
  No, the signals are not
  Presumably security measure from car manufacturers
  Boo!

## Slide 29: Getting Data From The CAN Bus
A search of the internet revealed some useful information
Where There’s A Will There’s A Way
Wire Colour | Signal
Orange/Brown | CAN Low (for all buses)
Orange/Black | CAN Hi (Powertrain bus)
Orange/Green | CAN Hi (Convenience bus)
Orange/Violet | CAN Hi (Infotainment bus)

## Slide 30: Getting Data From The CAN Bus
Where There’s A Will There’s A Way

## Slide 31: Getting Data From The CAN Bus
Where There’s A Will There’s A Way

## Slide 32: Getting Data From The CAN Bus
Where There’s A Will There’s A Way

## Slide 33: Getting Data From The CAN Bus
Where There’s A Will There’s A Way
Success!
(And the car still works)

## Slide 34: Getting Data From The CAN Bus
Lawicel CAN bus to USB
Serial device
Sends decoded data
Need to write a Java library
  CAN id
  Message data
Then the hard part starts
  Figuring it all out
Electrical Connectivity Is Only The Start

## Slide 35: Finished Data Capture System

## Slide 36: Heads Up Display/Telematics
Notes: This slide can also be used as a Q and A slide

## Slide 37: In Car Heads Up Displays Are Becoming A Reality
Jaguar Virtual Windscreen
Continental
Mini Cooper
NavTy

## Slide 38: Build Your Own HUD
Turns out it’s not that simple
First iteration
  3M MPro110 Micro Projector, half silvered film (from a cheap in-car HUD)
Didn’t really work
  Too much reflection of projector lamp, not image

## Slide 39: Build Your Own HUD
Second Attempt

## Slide 40: Raspberry Pi Heads Up Display
Cheap screen for the Pi
Use teleprompter glass rather than half-silvered perspex
  70% transmission, 30% refection much better
Issue: How to produce an inverted image?
Answer: Use a refection effect
Reflection ref = new Reflection();
ref.setFraction(1.0);
ref.setBottomOpacity(1.0);
ref.setTopOpacity(1.0);

## Slide 41: Data Display On HUD
Speed and engine RPM
  Use OBD2 data
  Wi-Fi dongle to access ELM327
Convert position (from GPS) into current speed limit
  Bluetooth dongle for pairing with mobile phone
  Configure Linux to provide network access via TCP/IP
  Transmit position obtained from GPS
  Write servlet to run on home Linux box (open port on firewall)
  Servlet uses position and Ordanance Survey data to determine speed limit
  (Future project)

## Slide 42: Hardware In Place

## Slide 43: Driver Analysis
Notes: This slide can also be used as a Q and A slide

## Slide 44: Display Collected Data
JavaFX application
Video stream
  Synchronised to data streams
Data recorded as sequence of text records
  Comma separated values
  One line per sensor
  Time stamp
Read all data in at start of application
  15 minutes of data takes about 100ms

## Slide 45: Synchronisation Issue
Configured system to collect data four times a second
Thread.sleep(250), right?
Not quite
Data acquisition and storage doesn’t happen instantaneously
  Raspberry Pi has limited resource footprint
  Takes around 6ms to grab all data and write it to text file
  Didn’t take this into account
  Each minute data falls 1.4 seconds behind video
Apply a fudge factor correction during playback

## Slide 46: Data To Display
Video (with controls)
G-forces
GPS co-ordinates/altitude
Map of current position
Speed (compare car and GPS)
Bearing
Engine load
Fuel pressure
Air intake temperature
Coolant temperature
Catalyst/exhaust temperature
Tyre temperature
Brake temperature
Throttle position
Engine RPM
Heart rate

## Slide 47: User Interface Design
Use JFXtras library (Gerrit Grunwald’s dials and LEDs)
Formula 1 style
  Throttle/brake/engine/gear display
  LED tachometer
Heart rate number is not too exciting
  Animations
  Continuous pulses was a bit of a challenge (several parallel, offset transitions)
JavaFX

## Slide 48: Conclusions and Resources
Notes: This slide can also be used as a Q and A slide

## Slide 49: Conclusions
Cars produce lots of data
Use of sensors with Java is simple to collect (most) data
Playback of data useful for insurance, fleet management, training
Java and JavaFX make UI design simple

## Slide 50: Resources and Links
www.sparkfun.com
www.adafruit.com
www.raspberrypi.org
blogs.oracle.com/speakjava
Twitter: @speakjava

## Slide 51: Demos
Notes: This slide can also be used as a Q and A slide