## Slide 1
ICS/SCADA Security
Analysis of a Beckhoff CX5020 PLC
Hans Hoefken

## Slide 2: About
Gregor Bonney
  Master Student at Aachen University of Applied Sciences (FH Aachen)
Hans Hoefken
  Research Assistant at FH Aachen
  Electrical Engineer, Ethical hacking, Pentesting
Benedickt Paffen
  Master Student at Aachen University of Applied Sciences (FH Aachen)
Marko Schuba
  Professor at FH Aachen
  IT-Security, IT-Forensics

## Slide 3: Agenda
Introduction
Structure SCADA System
Beckhoff CX 5020
TwinCAT
Automation Device Specification (ADS)
Security Investigation
Possible Attacks
Advisory for Suppliers

## Slide 4: Introduction
globalization of business
growing number of decentralized companies
  Industrial Control Systems (ICS) have to be network- and internet-enabled
essential part of ICS are SCADA systems
  Supervisory Control and Data Acquisition
there are known attacks
  number of attacks is growing

## Slide 5: CIA vs. AIC
IT Security
  confidentiality, integrity, availability
SCADA
  availability, integrity, confidentiality

## Slide 6: Design and Structure of a SCADA system
ERP
MES
SCADA
PLC/RTU
Sensor/Actuator
Enterprise Resource Planning
Manufacturing Execution System
Supervisory Control and Data Acquisition
Programmable Logic Controller
planning
retrieve data

## Slide 7: Design and Structure of a SCADA system

## Slide 8: Security of SCADA devices
not engineered with security in mind
not engineered with remote connections in mind
many are 15 years and older
new devices have built-in security, BUT…
  Beckhoff: 90% older systems in the field

## Slide 9: CX5020 – Brief overview
embedded PC
  Dual Core Atom processor
  1 GB RAM
  flashcard serving as persistent memory

## Slide 10: Operating system
customized Windows CE 6.0
keyboard and mouse
login password possible

## Slide 11: TwinCAT Devices
every device has a unique ADS-NetID
  enhancement of an IP address
  e.g. 192.168.1.100.1.1
for communication between devices a route needs to be established
ADS packets will be transported over TCP Port 48898 and UDP Port 48899
ADS-NetID
Transport-Address
Hostname
192.168.2.100.1.1
192.168.2.100
Device1

## Slide 12: Automation Device Specification
proprietary protocol from Beckhoff
used by TwinCAT (Management System)
optimized for throughput
encapsulated in TCP/IP
  or serial connections
no encryption
authorization

## Slide 13: System Control on CX5020
important Control Software
  CX Configuration Tool (FTP, VPN)
  Network and Dial-up Connection (IP)
  Password

## Slide 14: Security Analysis Results
nmap scan
  16 open ports
well known
unknown services
  48898 and 48899
  maintenance
  might be open in firewall

## Slide 15: Telnet
enabled by default
greeting phrase at start of the connection
  Welcome to Windows CE 6.0 Telnet service on CX-ABCDEF
    CX-ABCDEF is the hostname of the device (MAC in ASCII)
default username/password
  webguest/1
Windows CE 6.0 is a single user system
  all accounts get full administration privileges
    is able to create new accounts (CxAddUser)

## Slide 16: Webserver
index file
  Welcome to BECKHOFF CE device
special URL for administration interface
supports virtual directories
  exports different hard disk paths
  special URL for administration interface
    <ip>:5120/config

## Slide 17: Webserver: Virtual Directory
/remoteadmin
  Microsoft’s Windows CE remote management tool
not documented in Beckhoff’s manual
activated and not preconfigured
on first visit
  set a password
  gives full control
    network, time, file, and print server settings

## Slide 18: CE Remote Display
remote desktop service for Windows CE
listens on TCP port 987
connection requires password
connection setup transmitted in plaintext
attackable via ARP-Spoofing (mitm)
authenticated user has full control

## Slide 19: SCADA Service
Automation Device Specification (ADS)
  proprietary protocol
TwinCAT System Manager
  controls PLCs
    discover PLCs
    transmit programs to PLCs

## Slide 20: Test Setup
EtherCAT
TCP/IP

## Slide 21: ADS Search for Devices

## Slide 22: Search Devices
UDP Broadcast
  can also be sent to a dedicated IP
the ADS-NetID can be random

## Slide 23: Response
PLC answers with its own ADS NetID

## Slide 24: Creation of an ADS route
    Source WIN7VM-PC
    Destination CX5020 PLC
    no encryption
    username/password in plaintext
ADS packet header
ADS NetID
EWS hostname
Username
Password
EWS IP-Address

## Slide 25: Login in to CX5020
if password is wrong
  non zero error is returned (04 07)
if password is correct
  zero error code is returend (00 00)
packets can easily be reverse engineered
attackers can create their own ADS route
Error code
Error code

## Slide 26: Complete Message Flow

## Slide 27: Possible Attacks
use of virtual directory /remoteadmin
  after setting the initial password a new admin account is created
    create a new VPN account
No blocking after too many wrong passwords
  brute force/dictionary attack (UDP port 48899)
  PCL answers very fast 
  multiple connections in parallel possible
    Python script achieved ~8000 pw/sec
    Password allows full PLC control on port 987 & 48899

## Slide 28: Possible Attacks
Attack on VPN connection
  VPN connection to CX5020 with PPTP
  authentication with mschapv2
  mschapv2 is vulnerable
  steps of the attack
    mitm (with e.g. arpspoof)
    sniff connection establishment

## Slide 29: Possible Attacks
Attack on VPN connection
  VPN connection to CX5020 with PPTP
  authentication with mschapv2
  mschapv2 is vulnerable
  steps of the attack
    mitm (with e.g. arpspoof)
    sniff connection establishment
    brute force crack (e.g. with asleap)

## Slide 30: Attack mschapv2

## Slide 31: Possible attacks
USB Port
  WLAN adapter
    built-in driver support for WLAN adapter with RT2501 chip
    adapter is automatically connected
    choose a WLAN
      preconfigured registry entries are not used
    after connection all PLC-services are accessible
    bypass infrastructure firewalls (direct connection)

## Slide 32: Advisory for Suppliers
disable /remoteadmin virtual directory
disable telnet by default
limit number of ADS packets per second
deliver the device with strong passwords
delete WLAN drivers (if not used)
use alternative VPN technology

## Slide 33: Thank you!
Hans Hoefken
Aachen University of Applied Sciences
Germany
hoefken@fh-aachen.de