## Slide 1
Networking in the cloud: An SDN primer
Ben Cherian
Chief Strategy Officer
@bencherian
Midokura

## Slide 2
The current state of networking is too manual
Notes: Networking is not built for a self-service cloud world

## Slide 3
Telecom has this problem before

## Slide 4
Almon Strowger – mortician, inventor, and possibly paranoid
Notes: Patron saint of SDN
Undertaker from Topeka, Kansas
Rumor has it:
Almon believed calls sent to “the undertaker” weren’t being routed to him
Thought the competition had a relative working at the switching office
Moved to Kansas City. Thought the operators were giving his customers a busy signal
Became convinced that manual switching (with a switchboard operator) should be eliminated

## Slide 5
Strowger’s switches
Notes: Example of the Strowger switches
His work led to fully automated switching centers

## Slide 6
Wanted to solve:
Privacy
Intended human errors
Solved these too:
Unintended human errors
Speed of connections
Lowering operational costs of running a local exchange

## Slide 7
What is SDN?

## Slide 8
Traditional networks

## Slide 9
Control Plane:
Responsible for making decision on where the traffic is sent
Notes: Examples of control protocols:
ICMP
ARP
DHCP

## Slide 10
Data Plane:
Responsible for forwarding traffic to the selected destination

## Slide 11
The network needs better abstraction
Notes: Core concept in CS
Abstraction lends to good design, good scaling properties
OOP vs. Functional
Operating Systems

## Slide 12
A basic example of SDN

## Slide 13
SDN
IaaS Cloud
Fabric
Carrier/WAN
Cloud Service Providers
(CSP／CAP)
Enterprises
Definition
Example
Centralized control plane
Hardware solution for DC use
Juniper Qfabric
NEC Programmable Flow
Big Switch
Distributed control plane
Software solution for IaaS Cloud use
Midokura
VMWare/Nicira
Nuage
Hybrid control plane (CP)
  Distributed CP with BGP
  Centralized CP using OpenFlow
Google
Categories of SDN
Notes: 3 broad categories of SDN
  Virtual networking for or IaaS clouds
  Central control of data center network fabric
  Carrier network
    Replace or augment distributed signaling
    Edge only?

## Slide 14
ACLs
Stateful (L4) Firewall
  Security Groups
VPN
  IPSec
BGP gateway
REST API
Integration with CMS
  OpenStack
  CloudStack, etc.
Multi-tenancy
L2 isolation
L3 routing isolation
  VPC
  Like VRF (virtual routing and forwarding)
Scalable control plane
ARP, DHCP, ICMP
NAT (Floating IP)
Iaas Cloud Networking Requirements
Notes: The requirements for virtual networking for IaaS clouds are broad
  A variety of features

## Slide 15
Typical Network Topology
Iaas Cloud Networking Requirements
Notes: Typical virtual topology of OpenStack cloud
  Multiple projects/virtual data centers
  L2 isolation inside VDC
  L3 isolation between network, and between provider and tenants
    Just like in a real data center!
May want to connect customer site

## Slide 16
Traditional network
Centrally controlled OpenFlow based hop-by-hop switching fabric
Edge to edge overlays
Candidate models
Notes: Multiple candidates for IaaS virtual networking
  Each vendor touts their own solutions as being appropriate
Let’s examine them

## Slide 17
Ethernet VLANs for L2 isolation
  4096 limit
  VLANs will have large spanning trees terminating on many hosts
  High churn in switch control planes doing MAC learning non-stop
  Need MLAG for L2 multi-path
    Vendor specific
VRFs for L3 isolation
  Not scalable to cloud scale
  Expensive hardware
  Not fault tolerant
Traditional Network
Notes: Only option for L2 isolation in traditional network is VLAN
L3 isolation option is VRF or virtual appliance

## Slide 18
State in switches
  Proportional to virtual network state
  Need to update all switches in path when provisioning
  Not scalable, not fast enough to update, no atomicity of updates
Not good for IaaS cloud virtual networking
OpenFlow Fabric
Notes: doesn’t change the fact that the switches hold lots of network state
  Proportional to virtual domain network state

## Slide 19
Isolation not using VLANs
  IP encapsulation
Decouple from physical network
Provisioning VM doesn’t change underlay state
Underlay delivers to destination host IP
  Forwarding equivalence class (FEC)
Use scalable IGP (iBGP, OSPF) to build multi-path underlay
Inspired by VL2 from MSR
Edge to Edge IP Overlays
Notes: Physical network state doesn’t change
Virtual network state only at the edges
FEC

## Slide 20
Packet processing on x86 CPUs (at edge)
  Intel DPDK facilitates packet processing
  Number of cores in servers increasing fast
Clos Networks (for underlay)
  Spine and Leaf architecture with IP
  Economical and high E-W bandwidth
Merchant silicon (cheap IP switches)
      Broadcom, Intel (Fulcrum Micro), Marvell
      ODMs (Quanta, Accton) starting to sell directly
      Switches are becoming just like Linux servers
Optical intra-DC Networks
Market trends supporting overlay solutions
Notes: There are several trends supporting the edge to edge overlay model
Clos Network (spine and leaf) can be built with IP
  Standard and proven IGP
  Virtual network state only at edge
  Physical network config doesn’t change

## Slide 21
Logical Topology
Private IP Network
MN
MN
MN
Internet
BGP
Multi
Homing
Physical Topology
MN
VM
VM
MN
VM
VM
MN
VM
VM
BGP
To ISP3
BGP
To ISP2
BGP
To ISP1
vPort
Provider
Virtual
Router
Tenant A
Virtual
Router
Tenant B
Virtual
Router
Virtual
Switch A1
Virtual
Switch A2
Virtual
Switch B1
vPort
vPort
vPort
vPort
vPort
Network State Database
MN
MN
MN
Tunnel
Example of an overlay solution

## Slide 22: Overlays are the right approach!
But not sufficient.
We still need a scalable control plane.
Notes: I hope that you’re convinced that edge to edge overlays are the right approach to satisfy IaaS cloud networking requirements
But is that enough?
  Not quite.

## Slide 23
Questions?